## Slide 1: Installation / Setup
Unzip ‘probeitturn’ file, Installation path relative to Mach3 directory:
  C:\Mach3\turnaddons\probeitturn\
Mach3 must be in ‘radius’ mode (working on diameter mode for future release)
This version is a preliminary demo (and buggy?).
This version will accept a license fil, common with ProbeIt (mill version)

## Slide 2: Requirements
Mach3 ver 3.043.19 or later
Touch probe that activates ‘probe’ input to Mach3
  Touch probe orientation will depend on lathe configuration and item being probed.
  Tip ball center must be ‘on center’ for accurate results
Lathe axis configuration: Z+ towards tailstock, X+ equals larger diameter.
  Ref axis / angle definitions-->

## Slide 4
Basic ‘inputs’ required to run. Units are entered in native units (inches or mm, depending on user’s configuration)
This is for initial ‘touch off’ to set probe ball tip center relative to central axis. Measure actual DIAMETER, and enter RADIUS in ‘X surface value’ dro, then position probe tip near surface and hit button. Routine will probe part, and adjust the working X-DRO. Repeat for Z if desired

## Slide 5: Touchoff examples
X touchoff (OD)
Z touchoff (set Z left)
Use a gauge pin, or measure a specific diameter on part to be probed. Position probe tip manually near measured touchoff point (but not touching). Hit touchoff button desired, probe will touch, set DROs, then back off

## Slide 6
Basic ‘inputs’ that setup the probe direction and initial probe direction.
Either use one of the 4 ‘predefined’ spots,
or customize the start angle.
Basic ‘inputs’ required to run. Units are entered in native units (inches or mm, depending on user’s configuration). Note: Good starting point shown in inch units.
Hit button to start perimeter routine, after manually locating probe tip to start point.

## Slide 7
Basic ‘inputs’ required to run. Units are entered in native units (inches or mm, depending on user’s configuration). ‘Avg Probe Dia’ required. Cal table is not used in lathe version (to be deleted later)
This option, if turned on, will draw in a center line along the Z axis in DXF. Line will be drawn from –Z to + Z values (if values are both non-zero) or from -1000 to +1000 if values left zero.
These options allow recording of lines, points, or both in your DXF. Must have at least one on to record geometry.

## Slide 8: Output DXF
Note: Geometry in DXF is drawn in X-Z plane.
  Upon opening file, you will need to switch to a ‘front’ view to see geometry
Front view
Top view (as opened in Acad)